## Slide 1
THERMOELECTRIC
EFFECTS
The Science of Energy Conversion between Heat & Electricity
By Ehatasham Haque, Research Assistant (RA) to Dr. Nafisa Noor (NaNr) North South University, Dhaka.

## Slide 2
What Are Thermoelectric Effects?
Figure 2. Thermoelectric Generator Diagram.
Source: www.topmagneticgenerator.com
Figure 1. A Micro Thermoelectric Generator (μTEG).
Source: www.electronicsweekly.com

## Slide 3
The Three Thermoelectric Effects
SEEBECK
Heat → Electricity
1821
Thomas Seebeck
Temperature difference creates voltage
PELTIER
Electricity → Cooling/Heating
1834
Jean Peltier
Current flow creates temperature difference
THOMSON
Unified Theory
1851
William Thomson
(Lord Kelvin)
Connects all thermoelectric phenomena

## Slide 4
SEEBECK EFFECT
Definition:
Temperature gradient directly converts into electricity. Two dissimilar conductors generate voltage when subjected to heat difference.
Formula:
ES = −α∇T
Unit: μV/K
Figure 3. A generic setup diagram for Thermoelectric generator (TEG) showing Seebeck Effect in action.
Source: Gemini AI infused Image by Science ABC - Venkatesh Vaidyanathan.

## Slide 5
SEEBECK EFFECT: Real-World Applications
Thermocouples
Temperature Measurement
• Industrial processes
• Scientific research
• Manufacturing quality control
• Highly accurate and reliable
Power Generation
Thermoelectric Generators (TEGs)
• NASA spacecraft (Voyager, Mars rovers)
• Automotive waste heat recovery
• Remote sensors & IoT devices
• Industrial heat recovery

## Slide 6
PELTIER EFFECT
Definition:
Electric current creates heating or cooling at junctions. Heat absorbed at one junction, released at another - direction depends on current flow.
Formula:
QP = Π·I
Units: W (Watts) for heat
V (Volts) for coefficient
Historical Discovery
Discovered in 1834 by French physicist Jean Charles Athanase Peltier.
He found that electric current flowing through junctions of dissimilar metals either absorbed or released heat depending on current direction.
This was the inverse of Seebeck's discovery, unlocking thermoelectric cooling!

## Slide 7
PELTIER EFFECT APPLICATIONS
Cooling
Systems
Portable coolers, wine fridges, electronic component cooling
Industrial
Applications
Temperature control in manufacturing, lab equipment
Medical &
Scientific
PCR machines, medical refrigeration, precision instruments

## Slide 8
THOMSON EFFECT - The Unifying Theory
Definition:
Heating or cooling of a current-carrying conductor with a temperature gradient. Heat absorbed or released throughout the conductor, beyond Joule heating.
Formula:
qT = −K·J·∇T
Unit: V/K
THE KELVIN RELATIONS
William Thomson (Lord Kelvin) unified all three effects in 1851.
He proved that Seebeck, Peltier, and Thomson coefficients are interconnected through thermodynamic principles.
This completed the theoretical framework of thermoelectricity!

## Slide 9
Complete Thermoelectric Heat Balance
q = ρJ² + αJ∇T + τJ(dT/dx) − κ(d²T/dx²)
1. JOULE HEATING
ρJ² or I²R
Resistive losses (always positive)
2. PELTIER EFFECT
ΠI or αTJ
Heat at junctions (± reversible)
3. THOMSON EFFECT
τJ(dT/dx)
Heat along gradient (± reversible)
4. FOURIER CONDUCTION
−κ(d²T/dx²)
Thermal conduction (hot → cold)

## Slide 10
KEY TAKEAWAYS
1
SEEBECK: Heat → Electricity (Thermocouples, Power Generation)
2
PELTIER: Electricity → Cooling/Heating (Refrigeration, Electronics)
3
THOMSON: Unified Theory (Kelvin Relations connect all effects)
4
The Complete Thermoelectric equation that
governs all thermoelectric device performance

## Slide 11
COMSOL Simulation Checklist
1
Model Wizard
✓
2
Space Dimension
3
Select Physics
4
Select Study
5
Build Geometry
6
Declare Materials
7
Boundary Conditions
8
Mesh Generation
9
Compute Solution
✓
10
Post-Processing
✓
✓
✓
✓
✓
✓
✓
✓
✓
Checks Not Found…
Error 404!